## Slide 1: CSC 227 Computer Architecture and Organization I
SOLVED EXAMPLES: CACHE MAPPING FUNCTIONS

## Slide 2: DIRECT MAPPING FUNCTION
Formula
For Direct Mapping:
Cache Line=(Main Memory Block Number) mod (Number of Cache Address)
Format
Tag | Index | Offset​

## Slide 3: DIRECT MAPPING FUNCTION
Example 1: 0000, 0001, 0010….. 1111
Given
Main Memory = 64 KB
Cache Size = 1 KB (1024 bytes = 210 bytes = 10 bits)
Block Size/line size = 16 Bytes = 4bits
Find
Address bits of M/M
64KB = 216 bytes (1KB = 1024 BYTES = 210 BYTES)
26 X 210 = 216 = LOG2 216
Address bits:16

## Slide 4: DIRECT CACHE MAPPING
Find Offset Bits:
Offset Bits
16B = 24
Offset = 4 bits (0000, 0001, 0010…., 1111)
Find number of Cache lines:
Number of Cache Lines
1024 bytes/16 bytes ​= 64 lines (of size 16bytes each)
64 = 26
Index = 6 bits (number of bits used to identify each line)
(000000, 000001, 000010,……., 111111)

## Slide 5: DIRECT CACHE MAPPING
Find the number of Tag Bits
tag bit = total no. of m/m bits – ( index + offset)
Tag = 16 − 6 − 4
Tag = 6 bits
Address Format for cache
Tag Index Offset
6 bits 6 bits 4 bits
from cpu 000010 000011 1001 ( 2 , 3, 9)

## Slide 6: DIRECT CACHE MAPPING
5. Determine the Tag Directory Size
Tag Directory Size = Total cache lines x Tag Bits
64 × 6 = 384 bits
= 48 bytes (384/8)
Answer
Offset = 4 bits
Index = 6 bits
Tag = 6 bits
Tag Directory Size = 384 bits (48 bytes)

## Slide 7: DIRECT CACHE MAPPING
Example 2
Given
Main Memory = 128 KB
Cache = 4 KB
Block = 32 B
Find:
Offset
Index
Tag bits
Tag Directory Size
Example 3
Given
Main Memory = 1 MB
Cache = 8 KB
Block = 64 B
Find:
Offset
Index
Tag bits
Tag Directory Size

## Slide 8: FULLY ASSOCIATIVE CACHE MAPPING FUNCTION
What are the differences between the three cache mapping functions?
Direct = each block to exactly 1 line
Formula
Any memory block can be placed in any cache line.
Address Format
Tag | Offset ​
There is No index field

## Slide 9: FULLY ASSOCIATIVE MAPPING
Example 1
Given
Main Memory = 64 KB
Cache size = 1 KB
Block size/line size = 16 B
Address Bits
64KB = 216
Address = 16 bits
Find Offset bit
16B = 24
Offset = 4 bits
Tag
16−4 = 12 bits
Cache Lines
1024/16​ = 64 lines
Tag Directory
64 × 12 = 768 bits
= 96 bytes

## Slide 10: FULLY ASSOCIATIVE MAPPING
Example 2
Given
Main Memory = 256 KB
Cache = 4 KB
Block = 32 B
Find
Offset bits
Tag bits
Total Cache lines
Tag Directory Size
Example 3
Given
Main Memory = 2 MB
Cache = 16 KB
Block = 64 B
Find
Offset bits
Tag bits
Total Cache lines
Tag Directory Size

## Slide 11: SET ASSOCIATIVE MAPPING
Formula
For an n-way set associative cache: (8-way set associative)
Number of Sets = Cache Lines / n
Address Format
Tag | Set Index | Offset
​

## Slide 12: SET ASSOCIATIVE MAPPING
Example 1 (2-Way Set Associative)
Given
Main Memory = 64 KB
Cache = 1 KB
Block size = 16 B
2-Way Set Associative
Tag Bit = 16 – 5 – 4 = 7 bits
Tag Directory = 7 x 64 = 448 bits
= 56bytes
Address Bits
64KB = 26 X 210 = 16
Offset
16B = 24
Offset = 4 bits
Cache Lines
1024/16 = 64
Sets
64/2 = 32
Set Index = 5 bits

## Slide 13: SET ASSOCIATIVE MAPPING
Example 2 (4-Way Set Associative)
Given
Main Memory = 512 KB
Cache = 8 KB
Block = 32 B
4-Way
Find
Address bits
Offset
Cache lines
Set bit
Tag bits
Tag directory size
Example 3 (8-Way Set Associative)
Given
Main Memory = 4 MB
Cache = 32 KB
Block = 64 B
8-Way
Find
Address bits
Offset
Cache lines
Set bit
Tag bits
Tag directory size

## Slide 14: End of Unit