## Slide 2: MODULE 1 UNIT 2: OIL PALM PROCESSING

## Slide 3: INTRODUCTION
Oil palm processing involves mechanical and chemical operations for extracting crude palm oil (CPO) and palm kernel oil (PKO).

## Slide 4: Learning Objectives
Explain stages of processing
Importance of sterilization
Processes in kernel extraction
Factors affecting oil quality
Identify processing by‑products

## Slide 5: Fresh Fruit Bunch (FFB) Processing Stages
Sterilization
Threshing
Digesting
Pressing
Clarification

## Slide 6: Sterilization
Kills pathogens
Stops enzyme activity
Loosens fruits from bunch
Improves oil quality
Typical temp: 140–150°C for 60–90 minutes

## Slide 7: Threshing
Removes fruits from bunch stalks
Improves digestion efficiency
Threshing drum image

## Slide 8: Digesting
Breaks down mesocarp
Separates pulp from kernel
Improves oil extraction efficiency
see: FINIC, Palm Fruit Digester

## Slide 9: Pressing / Extraction
Uses screw press or hydraulic press
Extracts crude palm oil (CPO)
Manual Press for oil extraction

## Slide 10: Clarification
Separates fibre and sludge from oil
Uses water and heating
Stores clarified oil for packaging

## Slide 11: Palm Kernel Processing Stages
Fibre separation
Nut Drying
Nut Cracking
Kernel Oil Extraction
Storage

## Slide 12: Nut Drying
Reduces moisture content
Improves cracking efficiency
Methods: machine drying, hot platform, sun drying
Kernel Oil Extraction
Mechanical pressing
Chemical extraction methods
Oil stored in tanks
Nuts stored in jute bags

## Slide 13: Factors Affecting Oil Quality
Fruit ripeness
Sterilization temperature/time
Pressing conditions
Storage and handling practices
By‑products of Processing
Empty Fruit Bunches (EFB)
Palm Kernel Cake (PKC)
Palm Oil Mill Effluent (POME)

## Slide 14: Uses of By‑products
EFB: fertilizer & bioenergy
PKC: animal feed
POME: requires treatment before disposal

## Slide 15: Conclusion
Oil palm processing ensures production of edible oil, industrial raw materials, and valuable by‑products.

## Slide 16: Self‑Assessment Questions
Why is threshing important?
Mention two drying methods
Effects of poor storage
What is POME?
Suggest sustainable practices