## Slide 1: IFT222 Computer Architecture and Organization
COURSE OVERVIEW & GENERAL INTRODUCTION
Department of Computer and Information Sciences

## Slide 2
Module1:
Basic Concepts and Computer Evolution

## Slide 3
Course Overview

## Slide 4: Course Description
This course introduces the fundamental principles and structure of modern computer systems.
It covers the relationship between hardware and software, the organization of the CPU, memory hierarchy, input/output mechanisms, instruction execution, and performance measurement.
Students will learn how computers are designed, how they execute programs, and how architectural choices affect system performance.

## Slide 5: Course Objectives
By the end of this course, students should be able to:
Explain the internal structure of modern computer systems and how components interact to execute programs.
Analyze performance of computer systems using metrics like CPI, MIPS, and benchmarks.
Design simple assembly-level programs and understand instruction set architecture.
Understand memory hierarchy concepts, including cache, main memory, and virtual memory.
Describe processor design techniques including pipelining and basic parallelism.
Recognize I/O organization and fundamentals of storage and communication within computing systems.

## Slide 6: Course Learning Outcomes
By the end of this course, students will be able to:
Describe the fundamental components of a computer system and their roles.
Explain instruction set architecture and data representation techniques.
Analyze CPU performance using standard metrics.
Explain memory hierarchy and address translation mechanisms.
Describe processor implementation including pipelining and hazards.
Discuss I/O systems and peripheral communication techniques.
Apply assembly programming concepts to simple coding problems.
Evaluate architectural trade-offs for performance and cost.

## Slide 7: Recommended Textbooks
1. Computer Organization and Architecture, 11th Edition by William Stallings, Pearson Education, 2019, ISBN: 978-0134997193, Pages: ~1100
(One of the most widely used undergraduate textbooks).
2. Computer Organization and Design: The Hardware/Software Interface – David A. Patterson & John L. Hennessy. 5th/6th Edition (ARM or MIPS versions available) , Morgan Kaufmann, 2017+ (varies by edition), ISBN: 978-0128017333 (ARM edition)
3. Structured Computer Organization – Andrew S. Tanenbaum, 6th Edition, Pearson Education, 2013, ISBN: 978-0132916523
4. Essentials of Computer Organization and Architecture – Linda Null & Julia Lobur, 5th/6th Edition, Jones & Bartlett Learning, 2018+, ISBN: 978-1284123036
5. Computer Organization, Design, and Architecture – Sajjan G. Shiva, 6th Edition, CRC Press, 2025, ISBN: 978-1032805146

## Slide 8
UNIT 1:
FUNDAMENTALS OF COMPUTER ARCHITECTURE AND ORGANIZATION

## Slide 9: Introduction
Computers have had a huge impact on the manner in which society operates.
Increased efficiency, through automation and organization, only scratch the surface of what computing technology has afforded humanity.
In fact, the technology has progressed so much that people not utilizing computing technology in their businesses are at a disadvantage, as the computer today has an almost endless array of applications and functions.
This unit introduces the basic concepts of a computer generally in terms of what a computer is, parts of a computer and an overview of computer architecture and organization.

## Slide 10: Learning Outcomes
At the end of this Unit, you should be able to:
Describe a computer
Define computer architecture and computer organization.
Differentiate clearly between both concepts.
Explain the relationship between architecture and organization.
Identify components of each concept.
Apply the distinction to real-world computing systems.
Analyze how design decisions affect system performance.

## Slide 11: What is a Computer?
Many users of the computer know what the computer is used for as it applies to their field of endeavor.
But not everyone is able to give a proper definition of a computer.
The main subject of discussion in this course is the computer.
It is therefore important that we begin by providing a clear definition of this important tool.
Definition 1:
A computer is a programmable device that stores, retrieves, and processes data.

## Slide 12: What is a Computer?
Definition 2:
A computer is a machine or device that performs processes, calculations and operations based on instructions provided by a software or hardware program.
Definition 3:
A computer may be defined as a sophisticated electronic calculating machine that accepts data, processes the data according to a list of internally stored instructions and produces the resulting output information.

## Slide 13: Components of a Computer System
For the most part, all personal computers consist of the same basic components:
Central Processing Unit (CPU),
memory,
circuit board,
storage, and
input/output devices.

## Slide 14: Components of a Computer System

## Slide 15: Components of a Computer System
All computer applications make use of these components in different ways and combinations.
It also turns out that almost every digital device uses the same set of components, so examining the personal computer will give us insight into the structure of a variety of digital devices.
Thinking about computers in terms of their basic components, and the functionality associated with each component, reveals the primary functions of the computer in general.

## Slide 16: Computer System Design

## Slide 17: Computer System Design
Computer systems are designed using two closely related but distinct concepts namely:
Computer Architecture
Computer Organization
These concepts define how a computer system functions and operates internally.

## Slide 18: Computer Architecture
Computer architecture refers simply to the attributes of a computer visible to a programmer.
That is, it refers to those attributes that have direct impact on the logical execution of a computer program.
For example, it is an architectural design issue whether a computer will have a multiply instruction. (MULTIPLICATION UNIT)
But It is an organizational issue whether that instruction will be implemented by a special multiply unit or by a mechanism that makes repeated use of the add unit of the system

## Slide 19: Computer Architecture
Thus, computer architecture refers to the functional design and logical structure of a computer system. It describes the following aspects of a computer:
  Instruction set
  Data types
  Addressing modes
  Register organization

## Slide 20: Computer Architecture
Computer Architecture also answers the question: “What does the computer do?”.
It therefore serves as a blueprint for system design.
Examples of architectural attributes include the instruction set, the number of bits used to represent various data types (e.g., numbers, characters), I/O mechanisms, and techniques for addressing memory.

## Slide 21: In-Class Question
What is the primary focus of computer architecture?

## Slide 22: Answer
It focuses on the functional behavior and logical design of the computer system.

## Slide 23: Computer Organization
Computer organization refers to the operational units and their interconnections that realize the architectural specifications.
Organizational attributes include those hardware details transparent to the programmer, such as control signals; interfaces between the computer and peripherals; and the memory technology used.
Computer organization refers to the physical implementation of the system, including:
  Hardware components
  Interconnections
  Control signals
  Memory structure

## Slide 24: Computer Organization
Thus, Computer Organization answers the question: “How does the computer do it?. It ensures the architecture is translated into working hardware.
Computer architecture can be likened to a building design while computer organization may be likened to the actual construction or implementation of the building.

## Slide 25: In-Class Question
What does computer organization describe?

## Slide 26: Answer
It describes the physical arrangement and implementation of hardware components.

## Slide 27: Components of Computer Architecture and Computer Organization

## Slide 28: Computer Organization
A computer system is not just a collection of hardware parts; it is a carefully designed system governed by two fundamental concepts namely Computer Architecture and Computer Organization as discussed in previous section
These two concepts work together to define what a computer system does and how efficiently it performs task.
Understanding the components of these two vital concepts is crucial for designing efficient hardware systems, writing optimized software and Improving system performance.

## Slide 29: Components of Computer Architecture
Computer architecture defines the logical structure and functional behavior of a computer system.
These components are typically visible to programmers and determine how software interacts with hardware.

## Slide 30: Components of Computer Architecture - 1
Instruction Set Architecture (ISA)
The Instruction Set Architecture (ISA) is the core of computer architecture.
It acts as the interface between hardware and software and defines the following:
The set of instructions a processor can execute
  Instruction formats (e.g., ADD, LOAD, STORE)
  Data types (integer, floating point)
  Registers available
  Addressing modes

## Slide 31: Components of Computer Architecture - 1
Real-Life Applications
Software Compatibility
Applications compiled for a specific ISA (e.g., x86 or ARM) will only run on processors supporting that ISA. Example: Mobile apps are built for ARM-based processors in smartphones.
Operating Systems An OS is designed for a specific ISA.
Example: Windows OS is optimized for x86 architecture systems.
Different organizations (hardware implementations) can support the same ISA but vary in performance.

## Slide 32: Components of Computer Architecture -1
Real-Life Applications
Software Compatibility
Applications compiled for a specific ISA (e.g., x86 or ARM) will only run on processors supporting that ISA. Example: Mobile apps are built for ARM-based processors in smartphones.
Operating Systems An OS is designed for a specific ISA.
Example: Windows OS is optimized for x86 architecture systems.
Different organizations (hardware implementations) can support the same ISA but vary in performance.

## Slide 33: Components of Computer Architecture - 2
Data Types and Representation
Defines how data is stored and interpreted:
Integer formats (signed/unsigned)
Floating-point representation
Character encoding (ASCII, Unicode)

## Slide 34: Components of Computer Architecture - 2
Real-Life Applications
Financial Systems Accurate floating-point representation is critical for banking software.
Multimedia Systems Video and image processing rely on data formats (e.g., RGB encoding).
Scientific Computing Precision in floating-point calculations is essential for simulations.

## Slide 35: Components of Computer Architecture - 3
Addressing Modes
Addressing modes determine how operands are accessed during instruction execution.
Examples:
Immediate addressing
Direct addressing
Indirect addressing
Register addressing

## Slide 36: Components of Computer Architecture - 3
  Real-Life Applications of Addressing Modes
Efficient Program Execution Compilers choose addressing modes to optimize speed.
Embedded Systems Efficient memory access is crucial in devices with limited memory.
Gaming Systems Fast memory access improves frame rates and responsiveness.

## Slide 37: Components of Computer Architecture - 4
Register Set
Registers are small, fast storage locations inside the CPU.
Types include:
General-purpose registers
Special-purpose registers (Program Counter, Stack Pointer)

## Slide 38: Components of Computer Architecture - 4
Real-Life Applications of Register Sets
High-Speed Computation Programs execute faster when data is stored in registers instead of memory.
Real-Time Systems Critical systems (e.g., air traffic control) rely on fast register operations.
Mobile Devices Efficient register usage improves battery life and performance.

## Slide 39: Components of Computer Architecture - 5
System Design (e.g., Von Neumann vs Harvard)
Defines how memory and processing units are structured.
Von Neumann Architecture: Shared memory for data and instructions
Harvard Architecture: Separate memory for data and instructions

## Slide 40: Components of Computer Architecture - 5
Von Neumann Architecture: Shared memory for data and instructions
This processor configuration consists of a control unit, an arithmetic logic unit, a register set, and a memory region containing program instructions and data.
The key feature distinguishing the von Neumann architecture from the Harvard architecture is the use of a single area of memory for program instructions and the data acted upon by those Instructions.

## Slide 41: Components of Computer Architecture - 5
It is conceptually straightforward for programmers, and relatively easier for circuit designers, to locate all of the code and data a program requires in a single memory region. Figure 1 shows the elements of Von Neumann architecture.

## Slide 42: Components of Computer Architecture - 5
Harvard Architecture: Separate memory for data and instructions
A strict Harvard architecture uses one address space and memory bus for program instructions and a separate address space and memory bus for data.
This configuration has the immediate benefit of enabling simultaneous access to instructions and data, thereby implementing a form of parallelism.
This enhancement comes at the expense of essentially duplicating the number of address lines, data lines, and control signals that must be implemented by the processor to access both of the memory regions.

## Slide 43: Components of Computer Architecture - 5
The following diagram shows the layout of a processor implementing the Harvard architecture. Figure 2 shows the diagram of Harvard architecture.

## Slide 44: Components of Computer Architecture - 5
Real-Life Applications
Von Neumann Systems Used in general-purpose computers (laptops, desktops).
Cache memory, introduction of DDR memories, Pre-fectching, PIM,
Harvard Systems Used in microcontrollers and embedded systems for faster access.
Example: Microcontrollers in washing machines or cars use Harvard architecture.

## Slide 45: Components of Computer Organization

## Slide 46: Components of Computer Organization - 1
Computer organization deals with how architectural features are physically implemented.
1. Control Unit
Explanation: The control unit coordinates all operations of the CPU by:
  Fetching instructions
  Decoding instructions
  Generating control signals

## Slide 47: Components of Computer Organization - 1
Real-Life Applications
  Processor Execution:
Every program relies on the control unit for execution.
  Industrial Automation:
Machines operate based on control signals.
  Robotics Systems:
Controls sensors and actuators.

## Slide 48: Components of Computer Organization - 2
2. Arithmetic Logic Unit (ALU)
The ALU performs:
  Arithmetic operations (addition, subtraction)
  Logical operations (AND, OR, NOT)
Real-Life Applications:
  Digital Calculators: perform arithmetic operations.
  Gaming Systems: physics calculations depend on ALU.
  Artificial Intelligence Systems: neural network computations involve massive arithmetic operations.

## Slide 49: Components of Computer Organization - 3
3.Memory Organization
Memory is organized hierarchically:
  Cache (fastest)
  Main memory (RAM)
  Secondary storage
Real-Life Applications
  Smartphones: faster app performance depends on efficient memory hierarchy.
  Web Browsers: cache memory speeds up page loading.
  Cloud Systems: efficient memory usage supports large-scale computing.

## Slide 50: Components of Computer Organization - 4
4. Input/Output (I/O) Systems
Handles communication between the computer and external devices.
Real-Life Applications
  User Interaction: keyboard input and monitor output.
  Medical Devices: sensors provide input, displays provide output.
  Smart Homes: devices communicate with environmental sensors.

## Slide 51: Components of Computer Organization - 5
5. System Buses and Interconnections
  Buses transfer: Data Addresses and Control signals
Types:
  Data bus
  Address bus
  Control bus

## Slide 52: Components of Computer Organization - 5
Real-Life Applications
  Motherboard Communication: all components communicate via buses.
  Gaming Computers: High-speed buses improve graphics performance.
  Servers: efficient data transfer supports multiple users.

## Slide 53: Components of Computer Organization - 6
6. Pipelining and Parallelism
Pipelining: Overlapping instruction execution
Parallelism: Executing multiple tasks simultaneously
Real-Life Applications
Modern CPUs: execute multiple instructions at once.
Multicore Processors: enable multitasking.
AI and Big Data Systems: handle massive computations efficiently.

## Slide 54: INTEGRATED VIEW: ARCHITECTURE VS ORGANIZATION - 1
Real-Life Integrated
Example: Smartphone
Architecture defines:
Instruction set
Data types
Organization determines:
Speed
Battery life
Multitasking capability

## Slide 55: INTEGRATED VIEW: ARCHITECTURE VS ORGANIZATION - 2
Laptops
Same architecture (e.g., x86)
Different organizations:
  Cache size
  RAM speed
  CPU cores
Result: Different performance levels.

## Slide 56: CONCLUSION
The components of computer architecture and organization are deeply interconnected.
While architecture provides the blueprint and capabilities, organization determines efficiency and performance.
Understanding both allows:
  Engineers to design better systems
  Programmers to write optimized code
  Organizations to build high-performance computing solutions

## Slide 57
End of Unit 1